## Slide 1: Radiogenomic Analysis of Glioblastoma with Deep Learning Techniques
01/17/2021
Yichong Wang
wangyichong@u.nus.edu

## Slide 2: Brief Introduction

## Slide 3: Glioblastoma
Glioblastoma (GBM) is a highly aggressive adult brain tumor and the deadliest brain tumor that originates in glial cells.
A high degree of heterogeneity in both space and time
  Do not respond well to prescribed therapy because therapy targets the entire tumor rather than specific genetic sub-regions.
Three main criteria to divide GBM subtypes
  The most common subtype we use in lab is Varhaak et al. research in 2010

## Slide 4: Radiogenomics
Image acquisition;
Image processing, including noise/artifact reduction, intensity and/or orientation standardization, coregistration of the multiparametric MRI scans
ROI definition using manual annotation or automatic segmentation
Feature extraction based on human-engineered (conventional radiomics) or deep-learning approaches
Data analysis, involving machine/deep-learning methods for feature selection, classification, and cross-validation

## Slide 5: Progress made to-date

## Slide 6: Segmentation Result
Region-based Approaches
Edge-Based Approaches
Classification approaches
Altas-based approcahes

## Slide 7: Segmentation Result
U-net
Left: MRI Image, Middle: Ground Truth, Right: Semgentation Results
Dataset: 39 Patients
MRI Series: T1,T2,FLAIR
Plane: AX, COR, SAG
Totally 18528 Images
Train : Test = 4 : 1
Train times: 225248
Sensitivity and Specificity:
Confusion Matrix of all image segmentation results
Sensitivity> 95%

## Slide 8: Feature Extraction
In the feature Extraction procedure, we apply conventional CV method, using specific equation to calculate features to put image information from 2D to 1D
At first, I use my own code to calculate features, but the speed is slow. Right now, we use pyradiomics module to extract features from ROI
Pyradiomics have 120 features, most of them are texture features.
The most classical texture feature design is using GLCM

## Slide 9: Classify GBM Subtypes
Need Normalize before PCA
Decision Tree:
Original Data
PCA Data (99% information)
PCA Normalized Data

## Slide 10: Classify GBM Subtypes
Decision Tree: 56%
Overview:
Random Forest: 77%
MLP: 80%
Linear SVM: 40%
MLP have the best preference in classifying this dataset
This dataset is not linear relationship

## Slide 11: Classify GBM Subtypes Problems
Overfit:
Even add random forest tree numbers into 500, the overfit question still exist (Train accuracy = 100%)
This problem exist in every algorithms I have ever tried

## Slide 12: Classify GBM Subtypes Problems
Imbalance:
Data Imbalance, the Classical and Proneural is the most subtypes of GBM, leading to data imbalance,
which may lead classical and proneural type prediction sensitivity is higher, but others will be lower

## Slide 13: Classify GBM Subtypes Problems
Decision Tree: 68%
Random Forest: 84%
MLP: 88%
Linear SVM: 54%
Because one GBM cancer in one patient have different subtypes in different subregions, using two subtypes combined into a tuple as a label is very not scientific

## Slide 14: Future Plan

## Slide 15: Improvements and Other direction
For segmentation, considering we use different MRI series as one single input, I don’t think it will be a great way to train model, I will use one single MRI series picture to train specific model to detect the specific MRI series image. Meanwhile, we can also stack different MRI series picture in the axis=0 to make it a multi-channel picture to train the model, this can be helpful when we can obtain different MRI series pictures to do the segmentation.
For data imbalance leading to some subtypes’ sensitivity are so high to affect whole model’s accuracy problem, we can use data augmentation to solve. If we want to get better results, may be we can use GAN to produce data to do data augmentation.
For overfit problem, we need to try some optimizer methods to solve this problem.I think add dropout layer to MLP may solve this problem
At last, the most interesting improvements for this project is to remake the whole procedures to make a end-to-end networks. Because extract features from ROI byhuman design will definitely loss information of the radiographic phenotypes, the end-to-end network may be a great improvements.
Gene mutation
Gene expression profile